Specifications -  Peavey® Elements™ 212C Sub

Frequency range (-10 dB, half space ):

45 Hz – 1.5 kHz

Frequency Response, 1 meter on-axis, swept-sine in anechoic environment:

63Hz – 1 kHz (±3 dB)

Power Handling:

1000W Continuous, 2000W Program, 4000W peak.

Sound Pressure Level, 1 Watt, 1 meter in anechoic environment:

98 dB SPL , (2.00 V input)

Maximum Sound Pressure Level (1 meter):

128 dB SPL continuous

134 dB SPL peak

Transducer Complement:

2x 12in. Woofer, Vented

1208-8 SPS WR Water-Resistant Black Widow® Woofer

Box Tuning Frequency:

59 Hz

Input Connections:

2x Neutrik® Speakon® NL4MD & 1x 4-position barrier strip

Enclosure Materials & Finish:

Cabinet is constructed with 1 / 2” thick advanced technology composite fiber panels, coated in our black Hammerhead™ poly-urea with a lightly textured finish.  Triple-layer moisture-repellant grille assembly, consisting of an  perforated stainless steel outer grille, with inner hydro-phobic cloth mesh, and a proprietary third layer.

Dimensions (H x W x D):

29.44in. x 14.07 in. x 16.35 in.

748 mm x 357 mm x 415 mm

NOTE:  Depth does not include gland nut depth from weather-cover plate, or cable thickness.

Weight:

62 lbs.  (28.2 kg)

Mounting Provisions:

(12) 3/8"-16 Threaded Mounting Suspension Points (3 each top & bottom and 2 each sides & back).  Rubber washers are provided for use with 3/8” eyebolts, to assure a weather tight seal.

Three sets of 4) 1/4X20 SS inserts, the sets are located on the top, rear, and bottom for use with the Peavey® Versamount™ 70+ and the Peavey® Elements™ Pole Mount bracket.

Recommended Low Pass Filter:

Maximum frequency of 125 Hz, LR 24 dB/octave type.

Recommended High pass (Infrasonic) Filter:

45 Hz, LR 24 dB/oct. type.

NOTE:  To safely achieve maximum rated SPL output, audio signal must be filtered for extreme low frequency content.  All high SPL  vented cabinets should have this signal protection.

Features

Compact dual 12” Outdoor Fully-Weatherized Subwoofer Speaker System

Direct Radiator Vented Subwoofer Enclosure

Dual 12” Water-Resistant Black Widow® woofers, with a total of 2000 watts program power handling

Triple-layer perforated SS moisture-repellant grille

Versatile suspension provisions: 3/8” eyebolts or VM70 bracket or Pole Mount

Lighting/power pole mounting bracket fly point set

All external hardware is Stainless Steel

Enclosure is made of advanced technology composite fiber panels

Cabinet coated in black Hammerhead™ poly-urea finish.

Weather-sealed input cup cover with gland nut.

70 Volt transformer option available, easily upgraded in the field

Overall system weatherization rating of IP45

Description

The new Elements™ 212C Sub loudspeaker system from Peavey® Electronics provide unparalleled flexibility for permanent outdoor installations.  The Elements™ 212C Sub system is a dual woofer subwoofer speaker system comprised of a pair of 12” Water-Resistant Black Widow® woofers tuned for maximum low frequency output.

The Elements™ 212C Sub speaker system is constructed of 1 / 2 “ thick advanced technology composite fiber panels and are coated with a black Hammerhead™ poly-urea finish.  A 18 gauge powder-coated perforated stainless-steel metal grille with an inner hydro-phobic cloth mesh, and a foam third layer protects the front of the system from external moisture and dust.  A full set of twelve 3/8"-16 threaded mounting suspension points, 3 each top and 3 each bottom, and 2 each sides & back, is provided for flying and mounting, as well as three sets of 4) 1/4X20 SS inserts.  The sets of four are located on the top, rear, and bottom for use with the Peavey® Versamount™ 70+ and the Peavey® Elements™ Pole Mount bracket.

The Elements™ 212C Sub has a water-resistant version of the high power Black Widow® WR woofer incorporated, with a resin impregnated cone and dust cap for superior environmental stability.  Capable of over 1,000W of continuous power handling (AES Std 2-1984), the pair of weather-resistant woofers can handle a lot of sheer power.

Input connection to the system is made via a pair of 4 pin Neutrik® NL-4 connectors in parallel with a corrosion-resistant 4-position screw terminal strip for input connection flexibility while maintaining superior signal integrity.  A sealed cover plate with a gland nut protects the input cup connectors from the environment.

A field installed transformer option is available, providing an easy upgrade to 70V/100V transformer use.  The transformer is pre-mounted on a plate, the cover plate is unscrewed and removed from the Elements™ 212C Sub, and the plate mounted transformer installed in it’s place, with the simple un-plugging and plugging of water-proof connectors.  The transformer option available for the Elements™ 212C Sub has a 400W, 200W  and 100W output tap.

With it’s compact dimensions for a dual 12” enclosure, this system can put out some serious sound levels, and take large amounts of clean amplifier power, resulting in precise coverage with excellent clarity and high reliability.

Mounting

Contact Peavey Electronics Corp. for information and specifications for flying this speaker.

Architectural & Engineering Specifications

Elements™ 212C

The loudspeaker system shall have an operating bandwidth of 63 Hz - 1 kHz.  The nominal system output level shall be 98 dB when measured at a distance of one meter with an input of one watt.  The nominal impedance of the Elements™ 212C shall be 4 ohms.  The maximum continuous power handling of the system shall be 1,000 watts, maximum program power of 2,000 watts and a peak power input of at least 4,000 watts all with a minimum amplifier headroom of 3 dB and proper infrasonic filtering.

The enclosure shall be constructed of 1 / 2” weather-resistant advanced technology composite fiber panels, and finished in a textured hard-shell of black poly-urea coating.  The outside dimensions shall be 29.44 inches high by 14.07 inches wide by 16.35 inches deep.  The full-length grille shall have a triple-layer construction, consisting of perforated stainless steel outer layer, a hydrophobic cloth middle layer, and a reticulated foam inner layer, so as to provide excellent moisture protection to the drivers.  The weight shall be 62 pounds.  The loudspeaker system shall be a Peavey Elements™ model 212C Sub.

Features and specifications subject to change without notice.